## Slide 1: Vertical Farming Anishinabek Youth Ag Forum January 18, 2023
Fadi Al-Daoud, PhD
Greenhouse Vegetable Specialist
Ontario Ministry of Agriculture, Food and Rural Affairs (OMAFRA)
E-mail: fadi.al-daoud@ontario.ca
Phone: (519) 551-6703
Blog: ONGreenhouseVegetables.ca
LinkedIn: https://www.linkedin.com/in/fadi-al-daoud/

## Slide 2: OMAFRA’s Greenhouse Team
Dr. Fadi Al-Daoud – Production
Greenhouse Vegetable Specialist
Dr. Sarah Jandricic – IPM
Greenhouse Floriculture IPM Specialist
ONGreenhouseVegetables.ca
ONFloriculture.com
Cara McCreary – IPM
Greenhouse Vegetable IPM Specialist
Dr. Chevonne Dayboll – Production
Greenhouse Floriculture Specialist

## Slide 3: Where We Are and What We Do
Based out of Agriculture and Agri-Food Canada’s (AAFC) Harrow Research and Development Centre (Harrow, ON)
Portfolio includes food production in controlled environment agriculture (CEA) in Ontario
  Greenhouses (GH)
  Vertical farms (VF)
Work with producers, researchers and industry to advance CEA in Ontario
  Research
  Training and education (knowledge transfer and translation, KTT)

## Slide 4: Presentation Objective and Outline
Objectives:
Provide an overview of vertical farms (VF) in Ontario
Outline:
Vertical farming and sector overview
Production system
Research
University of Guelph

## Slide 5: What is vertical farming?
A form of controlled environment agriculture (CEA)
Growing food indoors
Light, temperature, water, fertilizer, humidity, air, etc. are all controlled
Lighting technologies like light-emitting diodes (LEDs) are making VF sustainable and profitable
Good Leaf

## Slide 6: Structure
Buildings: warehouses, store front, re-purposed buildings (barns)
Containers: retrofitted shipping containers
Good Leaf
Ortaliza
GR365N

## Slide 7: Location
Province-wide
Cluster in eastern Ontario
Agricultural, industrial, and commercial zones
Produced and consumed locally
Local workforce
Dryden
Timmins

## Slide 8: Production System
Horizontal surfaces: stacked vertically on shelves to maximize production.
Vertical surfaces: in what is commonly referred to as “grow walls” or “grow towers”. These towers stretch from floor to ceiling with plants growing on the side of them.
Undulating path: where one row of lights is present at the top of the growing environment and plants are rotated up and down to alternate their exposure to light and shade.
Zip Grow
Farmia
Vertical North

## Slide 9: Production System
Growing Media | Nutrient Solution | Environment Control
Soil: organic production Soil-less: rockwool, coconut coir, peat | Hydroponics: drip irrigation, nutrient film technique Aeroponics Recirculation and sterilization/filtration (UV systems most common) | Light Heat Humidity Air movement CO2 enrichment (not common)

## Slide 10: Environment Control Systems
Sensors
Central computer systems
Autonomous growing
Hort Americas

## Slide 11: Crops
Short production cycles (1-2 months to harvest)
Most common:
leafy greens (lettuce, arugula, kale, bok choy, mustard greens, swiss chard)
herbs (oregano, mint, basil, cilantro, fennel, parsley, rosemary)
microgreens
spinach
Coming soon:
fruiting crops (strawberries, mini-vegetables)
Good Leaf

## Slide 12: Recycled Nutrient Solution Schematic
Disinfection
fertilizer injector
leachate collection
greenhouse leachate sump pit
pump
dirty
leachate
tank
pump
fresh water intake
Element removal unit
clean leachate tank

## Slide 13
Chart: Microbe Species
| Botrytis cinerea | Fusarium spp. | F. oxysporum | F. solani | Olpidium bornovanus | O. brassicae | O. virulentus | Phytophthora spp. | P. cactorum | P. capsici | P. cinnamomi | P. cryptogea | P. drechsleri | P. fragariae | P. infestans | P. nicotianae | Pythium spp. | P. aphanidermatum | P. dissotocum | P. irregulare | P. polymastum | P. sylvaticum | P. ultimum | Rhizoctonia solani | Sclerotinia spp. | Thielaviopsis basicola | Verticillium spp. | V. albo-atrum | V. dahliae | V. dahliae (var longisporum)
Before UV | 0 | 8 | 5 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 3 | 3 | 7 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
After UV | 0 | 5 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Recirculated water DNA Scan Results from a pepper greenhouse using UV (Jan 2022, winter crop)
Fusarium
Pythium

## Slide 14
Chart: Microbe Species
| Botrytis cinerea | Fusarium spp. | F. oxysporum | F. solani | Olpidium bornovanus | O. brassicae | O. virulentus | Phytophthora spp. | P. cactorum | P. capsici | P. cinnamomi | P. cryptogea | P. drechsleri | P. fragariae | P. infestans | P. nicotianae | Pythium spp. | P. aphanidermatum | P. dissotocum | P. irregulare | P. polymastum | P. sylvaticum | P. ultimum | Rhizoctonia solani | Sclerotinia spp. | Thielaviopsis basicola | Verticillium spp. | V. albo-atrum | V. dahliae | V. dahliae (var longisporum)
Before UV | 0 | 7 | 5 | 0 | 0 | 0 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 10 | 3 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
After UV | 0 | 7 | 4 | 0 | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 6 | 0 | 10 | 4 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Fusarium
Pythium
Recirculated water DNA scan results from a warehouse vertical farm (grow wall) using UV (2022)

## Slide 15: Light Quantity and Distribution in a Vertical Farm
Chart: PPFD (umol/m2/sec)
| Total light
Front Middle | 120
Front Bottom | 98
Middle Middle | 111
Middle Bottom | 71
Back Middle | 103
Back Bottom | 84
Front Middle | 145
Front Bottom | 111
Middle Middle | 117
Middle Bottom | 110
Back Middle | 130
Back Bottom | 119
Left Side
Right Side

## Slide 16: Light Quality Changes with Intensity of Some Dimmable Lights
Chart: Ratio
| Red/Green | Red/Blue | Green/Blue
100% | 0.97835 | 2.4301 | 2.4839
75% | 1.0161 | 2.52 | 2.48
50% | 1.1613 | 3 | 2.5833
25% | 2.1667 | 6.5 | 3

## Slide 17: Summary: Benefits and Challenges of VF
Benefits | Challenges
More controlled growing environment and potential environmental sustainability | Limited crop selection
Brownfield sites and non-prime agricultural areas may be used | Electricity and natural gas prices
Smaller land footprint, reduce land use pressure | Technical expertise to install and manage and grower inexperience
Food is produced and consumed locally | Legacy as ‘niche’
Local workforce and skilled labour | Municipal plan policies and zoning of industrial uses may be inconsistent between municipalities

## Slide 18: Resources
OMAFRA’s Greenhouse Crops in Ontario website (http://omafra.gov.on.ca/english/crops/hort/greenhouse.html)
ONGreenhouseVegetables blog (https://ongreenhousevegetables.ca/)
  GrowON Webinar Series
Canadian Greenhouse Conference (https://www.canadiangreenhouseconference.com/)
Greenhouse Canada (https://www.greenhousecanada.com/)

## Slide 19: Vertical Farming in Northern Ontario
Fadi Al-Daoud, PhD
Greenhouse Vegetable Specialist
Ontario Ministry of Agriculture, Food and Rural Affairs (OMAFRA)
E-mail: fadi.al-daoud@ontario.ca
Phone: (519) 551-6703
Blog: ONGreenhouseVegetables.ca
LinkedIn: https://www.linkedin.com/in/fadi-al-daoud/